## Slide 1
2026 PRODUCT CATALOG

## Slide 2
2026 PRODUCT CATALOG
Ex-Sight.com is an Israeli technology company founded in 2008 and based in Tirat Carmel, Israel. Ex-Sight develops robust software-powered electro-optical systems for various markets.
We specialize in OEM integration, allowing partners to rebrand our products.

## Slide 3
DRI Performance: Theoretical Detection, Recognition and Identification ranges calculated according to the Johnson Criteria methodology. Actual performance may vary depending on atmospheric conditions, target characteristics, background contrast, sensor configuration and image-processing algorithms.

## Slide 4
DEEPSIGHT SOFTWARE Advanced Integrated Electro Optic Development Platform | 5
MICRO Miniature Rugged LWIR / Low Light Electro-Optic Sensor | 7
SITUATIONAL AWARENESS Rugged 360/180 Day & Night Electro-Optic Panoramic Staring System | 16
AVIGAIL Top-View 24/7 EO Payload | 20
DEEPSIGHT Integrated Electro-Optic Development Platform | 13
DEEPSPHERE Integrated Electro-Optic Development Gimbal | 26
SPHERE-SERIES Dual Sensor Rugged Gimbal | 30
PAN TILT Heavy Duty Stabilized Pan Tilt Positioners | 34
OZ SERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker | 49
FUSION SERIES Rugged Dual Sensor Driver Vision Enhancer (DVE) | 53
xEye Micro Rugged VIS/LWIR Single Sensor Driver Vision Enhancer (DVE) | 57
AIx SERIES Rugged AI Neural Processing Unit | 65
INTEGRATED ELECTRO-OPTICS PRODUCTS

## Slide 5: DEEPSIGHT SOFTWARE ADVANCED INTEGRATED ELECTRO OPTIC DEVELOPMENT PLATFORM
Advanced Multi-Sensor Electro-Optic Software Platform
Day & Night Electro-Optic Management with Automatic Target Recognition (ATR)
Enhanced Digital Video Tracking, classification, and detection
Precision PTZ, Day/Night, and LRF Control
Geo-Positioning with integrated route-tracking capabilities
INS GPS TRUE NORTH Gyro Stabilization
Electronic Image Stabilization (EIS)
Comprehensive ATR: detection, tracking, classification
Automated Fire Detection
Integrated Tracking, Simulation, and Training suite
Advanced Mapping and Field of View (FOV) zone visualization
Seamless Recording and system logging
External Integration with drones, radars, and third-party systems
Open-Source C# SDK & API for custom development

## Slide 6: Why DEEPSIGHT?
Unified Control: Centralized multi-sensor electro-optic software platform.
Smart Surveillance: Day/night management powered by Automatic Target Recognition.
Intelligent Tracking: Enhanced digital video classification and detection.
Full Hardware Mastery: Complete command over PTZ, day/night sensors, and laser rangefinders.
Smart Navigation: Real-time geo-positioning paired with pre-loaded route tracking.
Rock-Solid Stability: Dual INS/GPS True North gyro and electronic image stabilization.
Threat Detection: Built-in video analytics and automated fire alerts.
Ready to Train: All-in-one tracker, simulator, and operator training suite.
Situational Awareness: Dynamic mapping and Field of View zone visibility.
Complete Auditing: Continuous recording and system logging.
Unmatched Ecosystem: Easy integration with radars, drones, and external assets.
Developer Friendly: Open-source C# SDK/API for rapid customization.

## Slide 7
TOUGH
ETHERNET DUAL SENSOR MICRO GIMBAL
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 8
TOUGH
ETHERNET DUAL SENSOR MICRO GIMBAL
CHASSIS | 
MATERIALS | Internal: Aluminum, Cover: PETG-CF/ABS
DIMENSIONS | 116 x 68 mm, 370gr
LWIR SENSOR | 
DETECTOR | Uncooled VOx FPA
RESOLUTION | 640 × 512
PIXEL PITCH | 12 μm
FRAME RATE | 50 fps
SPECTRAL RANGE | 8 μm- 14 μm
FOCAL LENGTH OPTIONS | 6.8 / 9.1 / 13 / 19 / 25 mm
DIGITAL ZOOM | x8
DAY SENSOR | 
SENSOR | 5MP 1/2.5-inch PixelPlus2.2µm pixel
RESOLUTION | 2592 x 1944 (5MP) 30fps
WDR | 85db
SHUTTER | Rolling
LENS | 3.6mm / 6mm
AZIMUTH & ELEVATION | 2 Axes Movement, max. ±180 deg
PRECISION | 1 Deg
SPEED | Software Controlled
SOFTWARE INTERFACE | H.265/H.264 Ethernet/RTSP/ONVIF 1ststream: 1920×1080 / 1280×720 pixels 2ndstream: D1, VGA, 640×360 pixels
ELECTRIC INTERFACE | Pigtail open wires / RJ45 / Power
POWER | 12 VDC, Max 9W, Nominal 3.6W
FOV | 9.1 mm: 48.3° × 38.7°; 13 mm: 33.9° × 27.1°; 19 mm: 23.0° × 18.4°; 25 mm: 17.3° × 14.0°;
IMU | Optional

## Slide 9
DIMENSIONS: (mm) 116 x 68
WEIGHT: 370 g
9
TOUGH
ETHERNET DUAL SENSOR MICRO GIMBAL

## Slide 10
EX-SIGHT ADVANCED ELECTRO-OPTICS
FUSION
MICRO DUAL SENSOR ETHERNET ELECTRO OPTIC UNIT
MICRO

## Slide 11
CHASSIS | 
MATERIALS | PETG-CF or Aluminum
LWIR SENSOR | 
DETECTOR | Uncooled VOx FPA
RESOLUTION | 640 × 512
PIXEL PITCH | 12 μm
FRAME RATE | 50 fps
SPECTRAL RANGE | 8 μm- 14 μm
FOCAL LENGTH OPTIONS | 6.8 / 9.1 / 13 / 19 / 25 mm
DIGITAL ZOOM | x8
DAY SENSOR | 
SENSOR | 5MP 1/2.5-inch PixelPlus2.2µm pixel
RESOLUTION | 1920x1080 60 FPS
WDR | 85db
SHUTTER | Rolling
LENS | 3.6mm / 6mm
ETHERNET INTERFACE | H.265/H.264 Ethernet/RTSP/ONVIF 1ststream: 1920×1080 / 1280×720 pixels 2ndstream: D1, VGA, 640×360 pixels
ELECTRIC INTERFACE | D38999 / 24WB35PN (Cable mating connector 26WB35SN)
POWER | 9-36 VDC, 3W Nominal Consumption (250mA@12VDC)
FOV: | 9.1 mm: 48.3° × 38.7°; 13 mm: 33.9° × 27.1°; 19 mm: 23.0° × 18.4°; 25 mm: 17.3° × 14.0°;
4G Modem Module (Optional) | 
FUSION
MICRO DUAL SENSOR ETHERNET ELECTRO OPTIC UNIT
MICRO

## Slide 12
microFusion includes:
Day Sensor, LWIR Sensor, Bracket, Ethernet encoder, wired connectors.
FUSION
MICRO DUAL SENSOR ETHERNET ELECTRO OPTIC UNIT
MICRO
DIMENSIONS: (mm) 53x44x57.4 Ø14 Ø18.7
WEIGHT: 100 g (D38999 connector)

## Slide 13
EX-SIGHT ADVANCED ELECTRO-OPTICS
SITUATIONALAWARENESS
MICRO 180/360 ELECTRO-OPTIC PANORAMIC STARING SYSTEM
MICRO
Continuous panoramic surveillance across the visible and LWIR spectra, combining multi-sensor coverage, AI-assisted detection and tracking, and networked integration for manned and unmanned platforms.

## Slide 14
CHASSIS | 
MATERIALS | Powder Painted Aluminum
LWIR SENSOR | 
DETECTOR | 4x Uncooled VOx FPA
RESOLUTION | 640 × 512
PIXEL PITCH | 12 μm
FRAME RATE | 50 fps
SPECTRAL RANGE | 8 μm- 14 μm
FOV | 9.1 mm: 48.3° × 38.7°
DIGITAL ZOOM | x8
LOW LIGHT DAY SENSOR | 
SENSOR | 4 x 4K Day Camera IMX678
RESOLUTION | 3840x2160 (8MP) UHD 30fps
FOV | (H) 57.1° (V) 30.4° (D) 66.3°
SOFTWARE INTERFACE | H.265/H.264 Ethernet/RTSP/ONVIF
ELECTRIC INTERFACE | D38999/24WB35PN
POWER | 2A@24VDC (12-40VDC)
INS GPS IMU | Optional
SITUATIONALAWARENESS
MICRO 180/360 ELECTRO-OPTIC PANORAMIC STARING SYSTEM
MICRO

## Slide 15
15
DIMENSIONS: (mm) 53x44x57.4
SITUATIONALAWARENESS
MICRO 180/360 ELECTRO-OPTIC PANORAMIC STARING SYSTEM
MICRO

## Slide 16: SITUATIONALAWARENESS RUGGED ELECTRO-OPTIC PANORAMIC STARING SYSTEM FOR NAVAL AND GROUND APPLICATIONS
See First. Act First.
360°/180° 8MP 4K Day (VIS) & HD Night Continuous Coverage
AI-assisted Detection & Tracking
Modular Integration for Manned & Unmanned Platforms
Rugged Design, Hermetic Sealed IP-67, Nitrogen Purged
1Gbps Ethernet Interface, RTSP Streaming, Daisy Chain
12-40VDC Power Input
EX-SIGHT ADVANCED ELECTRO-OPTICS
Continuous panoramic surveillance across the visible and LWIR spectra, combining multi-sensor coverage, AI-assisted detection and tracking, and networked integration for manned and unmanned platforms.

## Slide 17: SITUATIONALAWARENESS RUGGED 360/180 DAY & NIGHT ELECTRO-OPTIC PANORAMIC STARING SYSTEM
 | SA360 | SA180
LOW LIGHT VIS DAY | SIX (6) x 3840*2160/30fps SONY Super Starlight IMX678 8.0MP 4K 30 FPS SAPPHIRE Window | THREE (3) x 3840*2160/30fps SONY Super Starlight IMX678 8.0MP 4K 30 FPS SAPPHIRE Window
DAY WINDOW | SAPPHIRE | 
FOV DAY | SIX (6) FOV (H) 93.1° (V) 49.6° (D) 110.8° Or FOV (H) 57.1° (V) 30.4° (D)66.3° | THREE (3) FOV (H) 93.1° (V) 49.6° (D) 110.8° Or FOV (H) 57.1° (V) 30.4° (D) 66.3°
NIGHT LWIR | SIX (6) 1280x1024 or 640x512 12μm 30 FPS GE Window AR/DLC | THREE (3) 1280x1024 or 640x512 12μm 30 FPS GE Window AR/DLC
NIGHT WINDOW | GE Window AR/DLC | 
FOV NIGHT LWIR | 420° Deg. (H) 6 x 70° FOV (H) 420° (V) 46° | 210° Deg. (H) 3 x 70° FOV (H) 210° (V) 46°
DETECTION (640x512) (1280x1024) | NATO/HUMAN 370m / 167m 830m / 375m | NATO/HUMAN 370m / 167m 830m / 375m
POWER | 2A@24VDC (12-40VDC) | 1A@24VDC (12-40VDC)
DIMENSIONS | 470x470x185 mm | 483x270x237 mm
ETHERNET | Embedded Industrial Gigabit Ethernet Switch | 
PNL CONNECTOR | Hermetic Stainless Steel D38999/23YD35PN | 
CABLE CONNECTOR | Hermetic Stainless Steel D38999/26KD35SN | 
WEIGHT (Kg) | 30 kg | 16 kg
CHASSIS | RUGGED CNC Structure, Aluminum Chassis, ANTI SALT BLACK POWDER PAINT | 
IP RATE | Sealed, IP67 Nitrogen Purged | 

## Slide 18: SITUATIONALAWARENESS FLAT VS. COMPACT DESIGN OPTIONS
SA180 - Horizontal Flat Horizontal, Side by Side 483x270x237 mm | SA180V - Vertical Compact Vertical Aligned 357x197x253 mm

## Slide 19: SITUATIONALAWARENESS
PIN | DESCRIPTION
1 | Main ETH 1 (White Orange)
2 | Main ETH 2 (Orange)
3 | Main ETH 3 (White Green)
4 | Main ETH 4 (Blue)
5 | Main ETH 5 (White Blue)
6 | Main ETH 6 (Green)
7 | Main ETH 7 (White Brown)
8 | Main ETH 8 (Brown)
9 | NC
10 | NC
11 | 12VDC
12 | GND
PIN | DESCRIPTION
13 | 12VDC
14 | GND
15 | Backup ETH 1 (White Orange)
16 | Backup ETH 2 (Orange)
17 | Backup ETH 3 (White Green)
18 | Backup ETH 4 (Blue)
19 | Backup ETH 5 (White Blue)
20 | Backup ETH 6 (Green)
21 | Backup ETH 7 (White Brown)
22 | Backup ETH 8 (Brown)
23-37 | NC
CABLE CONNECTOR PIN LAYOUT
D38999/26KD35SN Stainless Steel Hermetic Connector
Chart: Nyquist Detection Distance (NATO/Human) in meters
| 640x512 | 1280x1024
D (NATO) | 370 | 830
D (Human) | 167 | 375

## Slide 20: AVIGAIL360 360 DOME SITUATIONAL AWARENESS UAS DETECTOR
EX-SIGHT ADVANCED ELECTRO-OPTICS
See First. Act First.
360 (H) x 180 (V) deg Staring Detection System
Up to 42 Day/Night sensors for Continuous Coverage
ATR – Automated AI-assisted Detection & Tracking, made for counter drones
Modular Integration for Manned & Unmanned Platforms
Optional Fiber optic Ethernet interface for high transfer rates
Large area coverage
External Stabilized Power Supply
AVIGAIL is a standalone 42 sensors drone detection system. AVIGAIL integrates an array of 21 Low Light Day Visual sensors and 21 Uncooled LWIR 640x512 Night detector sensors providing 360 (AZ) x 180 (El) Deg Dome detection. The system is connected via Fiber optic or Ethernet Giga connection into an Array of NPU processors packaged in one single Chassis named AIxNPU4.
The Dome system constantly Monitors, Detects and Tracks 360 (Az) x 180 (El) deg and looking for drones. The detectors array (42 sensors) is connected to a fully automated computerized Neural processing unit which detects, tracks and position the threats in space.
AVIGAIL communicates with and provides position data to external tracking systems such as DEEPSIGHT or other counter drone systems in order to follow and eliminate the threats.

## Slide 21
AVIGAIL360
360 DOME SITUATIONAL AWARENESS DRONE DETECTOR
MODEL | AVIGAIL
SENSORS | AVIGAIL-4K: 21 x Day 4K 3840x2160 pixels IMX678 H.265 And / Or AVIGAIL-640: 21 x LWIR 640x512 pixels 12-micron H.265
SYSTEM COMPONENTS | IP66 Light Weight Case Rj45 1GB / Fiber Optic Ethernet Connector Embedded switch AI Hardware Software included
FOV | 360 Dome : 21 cams x (57.1°x 30.4°)
POWER | 9-75 VDC, 72W

## Slide 22: AVIGAILTOPVIEW WIDE-AREA SURVEILLANCE & SITUATIONAL AWARENESS PAYLOAD
See First. Act First.
18 x 4K Day (VIS) & Night LWIR Continuous Coverage, Wide-Area Surveillance
AI-assisted Detection & Tracking
Integrated investigation PTZ
Modular Integration for Manned & Unmanned Platforms
Fiber optic Ethernet interface for high transfer rates
Large terrain coverage 750m x 750m @ 100m alt
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 23
LOW LIGHT SENSOR | MODEL | AVIGAIL
 | LOW LIGHT SENSOR | 18 x Day 4K 3840x2160 pixels IMX678 H265 18 x LWIR 640x512 pixels 12 micron
 | SYSTEM COMPONENTS | IP66 Light Weight Case Fiber Optic Ethernet Connector Embedded switch Software included
 | FOV | 16 cams x (57.1°x 30.4°)
 | POWER | 9-75 VDC, 72W
AVIGAILTOPVIEW WIDE-AREA SURVEILLANCE & SITUATIONAL AWARENESS PAYLOAD

## Slide 24: DEEPSIGHT INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM
DETECT. IDENTIFY. DOMINATE.
SightDESK. complete software solution, control center application
Live Streaming. Fusion | Day | Night | Scene Real-Time Streams
Telemetry Data. Detectors, Trackers, LRF, Pan Tilt Data, INS
Geo-Position. INS, GPS, Compass, IMU, GYRO, Mapping
Fire-Detector. Day and Night fire risk detection
Storage. Video/Audio Storage Manager, Logger
Alerts. Alert manager. IO connectivity and LAN/WAN alerts
ATR. Target Detection / Tracking / PTZ Tracker
Stabilization. EIS (3 Axis Image) and Gyro Stabilization
Panorama. Panorama Generator. Live Field of View control, Presets
Customized GUI. Win forms or Web
Code. Ready to run Code examples and Open Source .Net software interface
Discovery Tool. Open-source discovery tool with your brand
Secured VLAN. with Single IP Address to the device
EX-SIGHT ADVANCED ELECTRO-OPTICS
DEEPSIGHT is an open, software-defined electro-optical command and control platform that unifies day, night, thermal, PTZ, LRF, INS/GNSS and AI-based analytics into a single operational environment. The platform provides real-time detection, tracking, classification, geo-positioning, recording and external-system integration through standard network interfaces and APIs.

## Slide 25
SIGHT IS QUALIFIED: MIL-STD-810G FOR THE FOLLOWING PROCEDURES:
High Temp. - Method 501.6, Procedure I Storage high temp 168H
Low Temp. - Method 502.6, Procedure I Storage low temp 24H
High Temp. - Method 501.6, Procedure II Operation high temperature 24H
Low Temp. - Method 502.6, Procedure II Operation low temp
Temperature Shock -Method 503.6,63/-33, 1 cycle
Vibration - method 514.7, transportation highway,1h each axis total 3h
Vibration - method 528.1, operational 15 sec each frequency, endurance 2h
Shock - method 516.7, Procedure I,40g/11ms
Dust -method 510.6, procedure I
Salt Fog, total 96h
SAND -Method 510.6, procedure II
Humidity - Method 507.6, Procedure II, 240H
Sealing test towards IEC60529 IP67 code
Solar radiation - Method 505.4 procedure I – 72h
Rain - Method 506.4, Procedure II, 15minutes
Fluids contamination - Method 504.3
MIL STD 461F EMI RFI CE101, CE102, CS101, CS114, CS116, RE101 RE102, RS101, RS103 (2Mhz-18Ghz;50V/m).
Tested by:
25
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 26
MODEL | MWIR 15-300 |  | LWIR 25-150 |  | LWIR 20-100 |  | LWIR HD 25-75 | 
LOW LIGHT DAY SENSOR | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2° Or 3.7MP SONY IMX675 Zoom Block Optical x40 Digital x32 Resolution 2560x1440 @ 30fps Focal Length 4.25mm-170mm FOV 73.8° - 2.16° |  |  |  |  |  |  | 
DAY WINDOW | SAPPHIRE |  |  |  |  |  |  | 
NIGHT SENSOR | COOLED MWIR 640x512 x20 Zoom 15-300 mm F4.0 FOV 1.83° to 35.5° |  | LWIR 640x512 x6 Zoom 25-150mm FOV 17,5° to 2,93° | LWIR 640x512 x6 Zoom 25-150mm FOV 17,5° to 2,93° |  | LWIR 640x512 x5 Zoom 20-100mm FOV 22,5° to 4,4° |  | LWIR 1280x1024 x3 Zoom 25-75mm FOV 32°to 10.9°
NIGHT WINDOW | GE/SILICON windows, Size: φ92.6x5mm, AR/DLC |  |  |  |  |  |  | 
MOUNTING | Horizontal / Vertical Installation |  |  |  |  |  |  | 
THERMAL DRI – Detection, Recognition, Identification |  |  |  |  |  |  |  | 
DETECTION (m) Human/NATO target |  | 8,660/14,500 | 4,300/9,583 |  | 2,886/6,388 |  | 2,165/4,791 | 
RECOGNITION (m) Human/NATO target |  | 4,330/9,583 | 2,165/4,791 |  | 1,443/3,194 |  | 1,082/2,395 | 
IDENTIFICATION (m) Human/NATO target |  | 3,247/7,187 | 1,623/3,593 |  | 1,082/2,395 |  | 812/1,797 | 
LRF Laser Range Finder |  | 8KM NATO Target, Precision 0.01 – 0.5 m, Beam divergence 0.6 mrad, Eye safe Laser Class 1 |  |  |  |  |  | 
NPU |  | CPU Intel® Core™ Ultra Processors ,RAM 64GB, SSD 1TB ,INTEL® ARC™ |  |  |  |  |  | 
POWER |  | 12-40 VDC 120W Max. MIL.STD704, MIL.STD810G POWER STABILIZER |  |  |  |  |  | 
DIMENSIONS (mm) |  | 190 x300x284 mm |  |  |  |  |  | 
INTERFACE |  | ETHERNET INTERFACE |  |  |  |  |  | 
CONNECTOR |  | Hermetic Stainless Steel D38999/23YC35PN |  |  |  |  |  | 
WEIGHT (Kg) |  | 9 kg |  |  |  |  |  | 
IP RATE |  | Sealed IP67 Nitrogen Purged |  |  |  |  |  | 
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 27
MODEL |  | MWIR HD 15-300 | SWIR HD 7.1-200 |  | SWIR HD 17-510 | LWIR HD 25-225
LOW LIGHT DAY SENSOR |  | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2° Or 3.7MP SONY IMX675 Zoom Block Optical x40 Digital x32 Resolution 2560x1440 @ 30fps Focal Length 4.25mm-170mm FOV 73.8° - 2.16° |  |  |  | 
DAY WINDOW |  | SAPPHIRE GLASS |  |  |  | 
NIGHT SENSOR |  | COOLED HD MWIR x20 Zoom 15-300 mm F4.0 FOV 35.5°to 1.83° | SWIR 1280x1024 x28 Zoom 7.1-200mm FOV 48.5° to 1.83° | SWIR 1280x1024 x28 Zoom 7.1-200mm FOV 48.5° to 1.83° | SWIR 1280x1024 x30 Zoom 17-510mm FOV 21.32° to 0.72° | LWIR 1280x1024 x9 Zoom 25-225mm FOV 34.2° to 3.9°
NIGHT WINDOW |  | GE/SILICON windows |  |  |  | 
MOUNTING |  | Horizontal / Vertical Installation |  |  |  | 
 | THERMAL DRI – Detection, Recognition, Identification |  |  |  |  | 
DETECTION (m) Human/NATO target |  | 8,660/14,500 | 13,856/30,666 |  | 35,333/78,200 | 6,495/14,375
RECOGNITION (m) Human/NATO target |  | 4,330/9,583 | 6,928/15,333 |  | 17,666/39,100 | 3,247/7,187
IDENTIFICATION (m) Human/NATO target |  | 3,247/7,187 | 5,196/11,500 |  | 13,250/29,325 | 2,435/5,390
LRF Laser Range Finder |  | 8KM NATO Target, Precision 0.01 – 0.5 m, Beam divergence 0.6 mrad, Eye safe Laser Class 1 |  |  |  | 
NPU |  | CPU Intel® Core™ Ultra Processors ,RAM 64GB, SSD 1TB ,INTEL® ARC™ |  |  |  | 
POWER |  | 12-40 VDC 120W Max. MIL.STD704, MIL.STD810G POWER STABILIZER |  |  |  | 
DIMENSIONS(mm) |  | 190x300x284 mm |  |  | 275x367x360 mm | 
INTERFACE |  | ETHERNET INTERFACE |  |  |  | 
CONNECTOR |  | Hermetic Stainless Steel D38999/23YC35PN |  |  |  | 
WEIGHT (Kg) |  | 12 kg | 16 kg |  | 20 kg | 23 kg
IP RATE |  | Sealed IP67 Nitrogen Purged |  |  |  | 
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)
27
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 28
MODEL | MWIR HD 50-1000 |  | LWIR HD 30-300 | LWIR HD 25-225 PRO |  | SWIR HD 17-510 PRO | 
LOW LIGHT DAY SENSOR | 1/1.8" 5MP Pregius S Global Exposure CMOS, 2448 × 2048, 5MP 20 ~ 1200mm；60× Optical, 16× Digital FOV 19.0° to 0.32° |  |  |  |  |  | 
DAY WINDOW | SAPPHIRE GLASS |  |  |  |  |  | 
NIGHT SENSOR | COOLED HD MWIR x20 Zoom 50-1000 mm F4.0 FOV 14.6° to 0.7° |  | LWIR 1280x1024 x10 Zoom 30-300mm FOV 32° to 10.9° |  | LWIR 1280x1024 x9 Zoom 25-225mm FOV 34.2° to 3.9 |  | SWIR 1280x1024 x30 Zoom 17-510mm FOV 21.32° to 0.72
NIGHT WINDOW | GE/SILICON windows |  |  |  |  |  | 
MOUNTING | Horizontal Installation |  |  |  |  |  | 
THERMAL DRI – Detection, Recognition, Identification |  |  |  |  |  |  | 
DETECTION (m) Human/NATO target | 34,000/76,000 | 8,660/19,166 |  |  | 6,495/14,375 |  | 35,333/78,200
RECOGNITION (m) Human/NATO target | 17,320/38,333 | 4,330/9,583 |  |  | 3,247/7,187 |  | 17,666/39,100
IDENTIFICATION (m) Human/NATO target | 12,990/28,750 | 3,247/7,187 |  |  | 2,435/5,390 |  | 13,250/29,325
LRF Laser Range Finder | 8Km or 17.6Km NATO Precision 0.01 – 0.5 m, Beam divergence 0.6 mrad, Eye safe Laser Class 1 |  |  |  |  |  | 
NPU | CPU Intel® Core™ Ultra Processors ,RAM 64GB, SSD 1TB ,INTEL® ARC™ |  |  |  |  |  | 
POWER | 12-40 VDC 120W Max. MIL.STD704, MIL.STD810G POWER STABILIZER |  |  |  |  |  | 
DIMENSIONS (mm) | 536x629x376 |  |  |  |  |  | 
INTERFACE | ETHERNET INTERFACE |  |  |  |  |  | 
CONNECTOR | Hermetic Stainless Steel D38999/23YC35PN |  |  |  |  |  | 
WEIGHT (Kg) | 60 kg | 55 kg |  |  | 30 Kg |  | 30 Kg
IP RATE | Sealed IP67 Nitrogen Purged |  |  |  |  |  | 
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)
28
DEEPSIGHT
Integrated Electro-Optic Development Platform

## Slide 29
MODEL | OWL | OWL225 | OWL1000 | OMEGA Ω
MOUNTING TYPE | U Mount | U Mount | U Mount | Ω (OMEGA) TOP + Sides
TILT | Max ±90° Deg Max. Motor Torque (NM) 35/ 50/ 150 |  |  | 
PAN | Cont. 360° Deg Motor Torque (NM) 35/ 50/ 150 |  |  | 
TRUE NORTH INS GPS | DUAL ANTENNA GNSS-AIDED INERTIAL NAVIGATION* |  |  | 
MAX.SPEED | 20 RPM, up to 120°/sec |  |  | 
MAX. PAYLOAD | 50 kg | 50 kg | 70 kg | 80 Kg
DIMENSIONS LxWxH (mm) | 416x210x442 | 505x255x624 | 777x765x629 | 794x210x419
WEIGHT(Kg) | 22 kg | 25 kg | 40 kg | 32 kg
IP RATE | IP66 |  |  | 
POWER | 24 - 48VDC |  |  | 
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 30
MODELS: MWIR15-300, LWIR 25-150, LWIR 20-100, LWIR HD 25-75, MWIR HD 15-300, SWIR HD 7.1-200, SWIR HD 17-510
DIMENSIONS: SIGHT (LxWxH, mm) 190x300x284
190
280
296
284
300
331
DEEPSIGHT
Integrated Electro-Optic Development Platform

## Slide 31
MODELS: MWIR15-300, LWIR 25-150, LWIR 20-100, LWIR HD 25-75, MWIR HD 15-300, SWIR HD 7.1-200, SWIR HD 17-510
DIMENSIONS: PT OWL (LxWxH, mm) 406x300x581
DEEPSIGHT
Integrated Electro-Optic Development Platform

## Slide 32
MODELS: MWIR15-300 , LWIR 25-150, LWIR 20-100, LWIR HD 25-75,
MWIR HD 15-300, SWIR HD 7.1-200, SWIR HD 17-510
DIMENSIONS: with PT OMEGA (LxWxH, mm) 402x300x608.5
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 33
MODELS: LWIR HD 25-225, SWIR HD 17-510
DIMENSIONS: SIGHT (LxWxH, mm) 275x367x360
331
DEEPSIGHT
Integrated Electro-Optic Development Platform

## Slide 34
MODELS: LWIR HD 25-225, SWIR HD 17-510
DIMENSIONS: with OWL225 (LxWxH, mm) 505x255x624
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 35
MODELS: MWIR HD 50-1000, LWIR HD 30-300, LWIR HD 25-225 PRO, SWIR HD 17-510 PRO
DIMENSIONS: (LxWxH, mm) 536x629x376
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 36
MODELS: MWIR HD 50-1000, LWIR HD 30-300, LWIR HD 25-225 PLUS, SWIR HD 17-510 PRO
DIMENSIONS: with OWL1000 PT (LxWxH, mm) 777x765x629
36
DEEPSIGHT
INTEGRATED ELECTRO-OPTIC DEVELOPMENT PLATFORM

## Slide 37: DEEPSPHERE INTEGRATED ELECTRO-OPTIC DEVELOPMENT GIMBAL
DETECT. IDENTIFY. DOMINATE.
SightDESK. complete software solution, control center application
Live Streaming. Fusion | Day | Night | Scene Real-Time Streams
Telemetry Data. Detectors, Trackers, LRF, Pan Tilt Data, INS
Geo-Position. INS, GPS, Compass, IMU, GYRO, Mapping
Fire-Detector. Day and Night fire risk detection
Storage. Video/Audio Storage Manager, Logger
Alerts. Alert manager. IO connectivity and LAN/WAN alerts
ATR. Target Detection / Tracking / PTZ Tracker
Stabilization. EIS (3 Axis Image) and Gyro Stabilization
Panorama. Panorama Generator.
Video-RADAR Automatic Detection/Tracking for Specified Zones
Customized GUI. Win forms or Web
Code. Ready to run Code examples and Open Source .Net software interface
Discovery Tool. Open-source discovery tool with your brand
Secured VLAN. with Single IP Address to the device
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 38
MODEL | MWIR 15-300 |  | LWIR 25-150 | LWIR 20-100 | LWIR HD 25-75
LOW LIGHT DAY SENSOR | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2° Or 3.7MP SONY IMX675 Zoom Block Optical x40 Digital x32 Resolution 2560x1440 @ 30fps Focal Length 4.25mm-170mm FOV 73.8° - 2.16° |  |  |  | 
DAY WINDOW | SAPPHIRE |  |  |  | 
NIGHT SENSOR | COOLED MWIR x20 Zoom 15-300 mm F4.0 FOV 1.83° to 35.5° |  | LWIR 640x512 x6 Zoom 25-150mm FOV 17,5° to 2,93° | LWIR 640x512 x5 Zoom 20-100mm FOV 22,5° to 4,4° | LWIR 1280x1024 x3 Zoom 25-75mm FOV 32°to 10.9°
NIGHT WINDOW | GE/SILICON windows, Size: φ92.6x5mm, AR/DLC |  |  |  | 
MOUNTING | Horizontal / Vertical Installation |  |  |  | 
Thermal DRI – Detection, Recognition, Identification |  |  |  |  | 
DETECTION (m) Human/NATO target | 8,660/14,500 |  | 4,300/9,583 | 2,886/6,388 | 2,165/4,791
RECOGNITION (m) Human/NATO target | 4,330/9,583 |  | 2,165/4,791 | 1,443/3,194 | 1,082/2,395
IDENTIFICATION (m) Human/NATO target | 3,247/7,187 |  | 1,623/3,593 | 1,082/2,395 | 812/1,797
LRF Laser Range Finder | 8KM NATO Target, Precision 0.01 – 0.5 m, Beam divergence 0.6 mrad, Eye safe Laser Class 1 |  |  |  | 
NPU | CPU Intel® Core™ Ultra Processors ,RAM 64GB, SSD 1TB ,INTEL® ARC™ |  |  |  | 
POWER | 48VDC External PSU |  |  |  | 
DIMENSIONS (mm) | 488.6x302x379.3 Ø300 base Ø302 |  |  |  | 
INTERFACE | ETHERNET INTERFACE, RTSP Streaming, DEEPSIGHT SDK |  |  |  | 
CONNECTOR | Hermetic Stainless Steel D38999/23YC35PN |  |  |  | 
WEIGHT (Kg) | 19,6 kg | 19,6 kg |  | 20 kg | 19,3 kg
IP RATE | Sealed IP67 |  |  |  | 
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)
DEEPSPHERE
INTEGRATED ELECTRO-OPTIC DEVELOPMENT GIMBAL

## Slide 39
MODEL | SWIR HD 7.1-200
LOW LIGHT DAY SENSOR | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2° Or 3.7MP SONY IMX675 Zoom Block Optical x40 Digital x32 Resolution 2560x1440 @ 30fps Focal Length 4.25mm-170mm FOV 73.8° - 2.16°
DAY WINDOW | SAPPHIRE GLASS
NIGHT SENSOR | SWIR 1280x1024 x28 Zoom 7.1-200mm FOV 48.5° to 1.83°
NIGHT WINDOW | GE/SILICON windows
MOUNTING | Horizontal / Vertical Installation
SWIR DRI – Detection, Recognition, Identification | 
DETECTION (m) Human/NATO target | 13,856/30,666
RECOGNITION (m) Human/NATO target | 6,928/15,333
IDENTIFICATION (m) Human/NATO target | 5,196/11,500
LRF Laser Range Finder | 8KM NATO Target, Precision 0.01 – 0.5 m, Beam divergence 0.6 mrad, Eye safe Laser Class 1
NPU | CPU Intel® Core™ Ultra Processors ,RAM 64GB, SSD 1TB ,INTEL® ARC™
POWER | 12-40 VDC 120W Max. MIL.STD704, MIL.STD810G POWER STABILIZER
DIMENSIONS (mm) | 488.6x302x379.3 Ø300 base Ø302
INTERFACE | ETHERNET INTERFACE
CONNECTOR | Hermetic Stainless Steel D38999/23YC35PN
WEIGHT (Kg) | 9 kg
IP RATE | Sealed IP67 Nitrogen Purged
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)
DEEPSPHERE
INTEGRATED ELECTRO-OPTIC DEVELOPMENT GIMBAL

## Slide 40
DIMENSIONS: (WxH, mm) 488.6x302x379.3 Ø300
base Ø302
40
DEEPSPHERE
INTEGRATED ELECTRO-OPTIC DEVELOPMENT GIMBAL

## Slide 41: SPHERESERIES DUAL SENSOR RUGGED GIMBAL
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 42: SPHERESERIES DUAL SENSOR RUGGED GIMBAL
MODEL |  | SPHERE-F | SPHERE-DUAL
LOW LIGHT DAY SENSOR |  | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2° | 3.0MP Global Shutter Zoom Block Optical x30 Digital x16 Resolution 2048x1536 @ 30fps Focal Length 5.5mm-165mm FOV 46.5° - 2.2°
DAY WINDOW |  | SAPPHIRE GLASS | 
NIGHT SENSOR |  | Single Sensor: LWIR 640x512 Up to 35mm, 12.5 deg | DUAL Sensor: 1st LWIR 640x512 5.8mm, 70 deg 2nd LWIR 640x512 60 mm, 7.3 deg
NIGHT WINDOW |  | GE/SILICON window | 
 | LWIR DRI Detection, Recognition, Identification |  | 
DETECTION (m) Human/NATO target |  | 35mm 1,010/2,236 | 60 mm 1,732/3,833
RECOGNITION (m) Human/NATO target |  | 35mm 360/798 | 60 mm 866/1,916
IDENTIFICATION (m) Human/NATO target |  | 35mm 270/599 | 60 mm 649/1,437
LRF Laser Range Finder |  | Up to 2KM NATO Target | N/A
POWER |  | 48 VDC external PSU | 
DIMENSIONS (mm) |  | 245x216x347 mm ⌀ 185 | 217x203x315.5 mm ⌀ 190
INTERFACE |  | ETHERNET INTERFACE, RTSP STREAMING | 
CONNECTOR |  | Hermetic Stainless Steel D38999/23YC35PN | 
WEIGHT (Kg) |  | 13 kg | 9 kg
IP RATE |  | Sealed IP67 | 
*DRI Calculation according to Johnson Criteria (Lines 3/6/8 D/R/I)

## Slide 43: SPHERESERIES DUAL SENSOR RUGGED GIMBAL
DIMENSIONS: (LxWxH, mm) 245x216x347 ⌀ 185

## Slide 44: SPHERESERIES DUAL SENSOR RUGGED GIMBAL
DIMENSIONS: (LxWxH, mm) 217x203x315.5 ⌀ 190

## Slide 45: HDPT-SERIES HEAVY DUTY STABILIZED PAN TILT POSITIONERS
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 46
HDPT-SERIES
HEAVY DUTY STABILIZED PAN TILT POSITIONERS
MODEL | OWL | OWL225 | OWL1000 | OMEGA Ω
MOUNTING TYPE | U Mount | U Mount | U Mount | Ω (OMEGA) TOP + Sides
TILT | Max ±90° Deg Max. Motor Torque (NM) 35/ 50/ 150 |  |  | 
PAN | Cont. 360° Deg Motor Torque (NM) 35/ 50/ 150 |  |  | 
TRUE NORTH INS GPS | DUAL ANTENNA GNSS-AIDED INERTIAL NAVIGATION* |  |  | 
MAX.SPEED | 20 RPM, up to 120°/sec |  |  | 
MAX. PAYLOAD | 50 kg | 50 kg | 70 kg | 80 Kg
DIMENSIONS LxWxH (mm) | 416x210x442 | 505x255x624 | 777x765x629 | 794x210x419
WEIGHT(Kg) | 22 kg | 25 kg | 40 kg | 32 kg
IP RATE | IP66 |  |  | 
POWER | 24 - 48VDC |  |  | 

## Slide 47
MODEL | ALMA | ADVA | COMPASS
MOUNTING TYPE | Top Mount | Top Mount | Top Mount
TILT | 35 NM | 35 NM | -
PAN | 35 NM | - | 35 NM
TRUE NORTH INS GPS | DUAL ANTENNA GNSS-AIDED INERTIAL NAVIGATION* | Optional VN100 INS/ VN200 INS | -
MAX.SPEED | 30 RPM, up to 180°/sec |  | 
MAX. PAYLOAD | 15 Kg | 9 Kg | 9 Kg
DIMENSIONS LxWxH (mm) | 218x163x296 | 232x210x158 | 
WEIGHT(Kg) | 8,5 kg | 3,5 Kg | 4,5 Kg
IP RATE | IP66 |  | 
POWER | 24-48VDC |  | 
PT-SERIES
LIGHT RUGGED STABILIZED POSITIONERS

## Slide 48
DIMENSIONS: without EO (LxWxH, mm) 442x416x210
WEIGHT: 22 kg
OWL-PT
HEAVY DUTY STABILIZED PAN TILT POSITIONER

## Slide 49
DIMENSIONS: with camera (LxWxH, mm) 544x416x210
OWL-PT
HEAVY DUTY STABILIZED PAN TILT POSITIONER

## Slide 50
DIMENSIONS: without camera (LxWxH, mm) 505x255x624
WEIGHT: 18 kg
OWL-PT
HEAVY DUTY STABILIZED PAN TILT POSITIONER

## Slide 51
DIMENSIONS with camera (LxWxH, mm) 484x505x210
OWL-PT
HEAVY DUTY STABILIZED PAN TILT POSITIONER

## Slide 52
DIMENSIONS with camera (LxWxH, mm) 777x765x629
OWL1000-PT
HEAVY DUTY STABILIZED U-SHAPED PAN TILT POSITIONER

## Slide 53
DIMENSIONS without camera (LxWxH, mm) 777x765x629
OWL1000-PT
HEAVY DUTY STABILIZED U-SHAPED PAN TILT POSITIONER

## Slide 54
DIMENSIONS without camera (LxWxH, mm) 794x210x419
WEIGHT 16 kg
OMEGA-PT
HEAVY DUTY STABILIZED Ω-SHAPED PAN TILT POSITIONER

## Slide 55
DIMENSIONS: with camera (LxWxH, mm) 218x163x296
WEIGHT: 8,6 kg
ALMA
HEAVY DUTY MINI STABILIZED PAN TILT POSITIONER

## Slide 56
ADVA
LIGHT RUGGED STABILIZED TILT
DIMENSIONS: without camera (LxWxH, mm) 218x210x158
WEIGHT: 3,5 kg

## Slide 57
ADVA-PT
LIGHT RUGGED STABILIZED TILT
DIMENSIONS: with camera OZ1280 (LxWxH, mm) 235x210x269
WEIGHT: with camera OZ1280 8,5 kg
DIMENSIONS: with camera Fusion640 (LxWxH, mm) 233x210x255
WEIGHT: with camera FUSION640 6kg
CAMERA OZ1280
CAMERA FUSION640

## Slide 58
COMPASS
LIGHT RUGGED STABILIZED PAN
DIMENSIONS: without camera (LxWxH, mm) 170x170x168,5 (+50)
WEIGHT: 4,5kg

## Slide 59
COMPASS
LIGHT RUGGED STABILIZED PAN
DIMENSIONS: with camera FUSION640 (LxWxH, mm) 170x198x306
WEIGHT: 7,8kg

## Slide 60: OZSERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker
ONESHOT
Up to 8.0MP 4K Day (VIS)
Up to HD 1280x1024 Night
Modular Integration for Manned & Unmanned Platforms
Rugged Design, Hermetic Sealed IP-67, Nitrogen Purged
Ethernet Interface, RTSP Streaming, Daisy Chain
12-40VDC Power Input
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 61
MODEL | OZ-1280-F | OZ-25-75 / HD
DAY SENSOR | GLOBAL SHUTTER X30 2048x1536 30 FPS H.265/H264 | GLOBAL SHUTTER X30 2048x1536 30 FPS H.265/H264
FOV DAY SENSOR | x30 ZOOM 4.5mm-162mm FOV (H) 59.0° to 2.4° | x30 ZOOM 4.5mm-162mm FOV (H) 59.0° to 2.4°
THERMAL SENSOR | UNCOOLED LWIR 12 μm 1280x1024 LENS 13mm 30 FPS FOV (H) 61° (V) 45,9° | UNCOOLED LWIR 12 μm 1280x1024 or 640x512 LENS 25-75 mm 1280x1024 FOV H*V (11,7°x8,8°~ 34,2°x25,6°) 640x512 FOV H*V (5,9°x4,4°~ 17,5°x13,1°)
LRF | 8 KM NATO TARGET | 8 KM NATO TARGET
 | LWIR DRI | 
DETECTION (m) NATO/HUMAN target | 830/375 | 4791/2165
RECOGNITION (m) NATO/HUMAN target | 415/187 | 2395/1082
IDENTIFICATION (m) NATO/HUMAN target | 311/140 | 1796/811
POWER | 9-36VDC, NOMINAL 5.6W (MAX on LOAD 12W) | 
DIMENSIONS (mm) | 198x173x111 | 240x200x130
CONNECTOR | Stainless Steel Hermetic Connector D38999/23YC35PN | 
WEIGHT (Kg) | 4.7 kg | 8 kg
IP RATE | IP67 Nitrogen Purged | 
OZSERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker

## Slide 62
DIMENSIONS: (LxWxH, mm) 198x173x111
WEIGHT: 4,7 kg
OZ1280 Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker

## Slide 63
OZ25-75/HD Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker
DIMENSIONS: (LxWxH, mm) 240x200x130
WEIGHT: 8 kg

## Slide 64: FUSIONSERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker
ONESHOT
Up to 8.0MP 4K Day (VIS)
Up to HD 1280x1024 Night
Modular Integration for Manned & Unmanned Platforms
Rugged Design, Hermetic Sealed IP-67, Nitrogen Purged
Ethernet Interface, RTSP Streaming, Daisy Chain
12-40VDC Power Input
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 65
MODEL |  | FUSION1280 | FUSION640
DAY SENSOR |  | 4K 8.0MP IMX678 3840x2160/30fps M12 LENS 30 FPS H.265/H.264/MJPEG | 4K 8.0MP IMX678 3840x2160/30fps M12 LENS 30 FPS H.265/H.264/MJPEG
FOV DAY SENSOR |  | DC DRIVE M12 FOV (H) 57° or 93° | DC DRIVE M12 FOV (H) 57° or 93°
THERMAL SENSOR |  | UNCOOLED LWIR 12 μm 1280x1024 LENS 13mm 30 FPS FOV (H) 61° (V) 45.9° | UNCOOLED LWIR 12 μm 640x512 LENS 5.8mm 30 FPS FOV (H) 67° (V) 50.3°
LRF |  | N/A | N/A
 | LWIR DRI |  | 
DETECTION (m) NATO/HUMAN target |  | 830/375 | 370/167
RECOGNITION (m) NATO/HUMAN target |  | 415/187 | 185/83
IDENTIFICATION (m) NATO/HUMAN target |  | 311/140 | 139/62
POWER |  | 9-36VDC, NOMINAL 5.6W (MAX on LOAD 12W) | 
DIMENSIONS (mm) |  | 149x147x96 | 147x117x96
CONNECTOR |  | Stainless Steel Hermetic Connector D38999/23YC35PN | 
WEIGHT (Kg) |  | 3 kg | 2.3 kg
IP RATE |  | IP67 Nitrogen Purged | 
FUSIONSERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker

## Slide 66
DIMENSIONS: (LxWxH, mm) 147x117x96
WEIGHT: 2,3 kg
SENSOR POSITIONING
HORIZONTAL
VERTICAL
FUSION640 Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker

## Slide 67
DIMENSIONS: (LxWxH, mm) 160x134x111
FUSION-F-BRKT-01
FUSION-F-BRKT-02
Bracket Options
FUSIONSERIES Rugged Day & Night Driver Vision Enhancer and Electro-Optic Tracker
DIMENSIONS: (LxWxH, mm) 190x187x120

## Slide 68: xEyeSERIES Rugged LWIR/Low Light Electro-Optic Sensor
EX-SIGHT ADVANCED ELECTRO-OPTICS

## Slide 69
MODEL | xEye-N Day | xEye-N LWIR | xEye-N LWIR | xEye-Z Day |  | xEye-Z LWIR | xEye
SENSOR | LOW LIGHT | UNCOOLED LWIR | UNCOOLED LWIR 12 μm 640x512 | LOW LIGHT |  | UNCOOLED LWIR | FULL HD
 | Up to 3840x2160 / 8MP 4K, IMX678 | 12 μm 640x512 |  | 2560x1440 x40 Zoom 4,25mm-170mm |  | 12 μm 1280x1024 LENS 13mm | 1920x1080 x36 Zoom 4 mm
 |  |  |  | LOW LIGHT |  | UNCOOLED LWIR | 
 |  |  |  | 2048x1536 x30 Zoom 5,5mm-162mm |  | 12 μm 1280x1024 LENS 9,8mm | 
FOV | LOW LIGHT FOV (4mm) (H) 93.1° (V) 49.6° (D)110.8° | LWIR FOV (5.8mm) FOV 69.4° x57.3° | LWIR FOV (5.8mm) FOV 69.4° x57.3° (4mm) FOV 88.4° x74.3° | LOW LIGHT FOV (4,25-170mm) FOV 73,8° to 2,16° |  | LWIR FOV (13mm) FOV 69.4° x 57.3° | LOW LIGHT FOV (4mm) H-FOV 90° V-FOV 46°
 | LOW LIGHT FOV (5 mm) (H)57.1° (V)30.4° (D) 66.3° | LWIR FOV (4mm) FOV 88.4° x74.3° |  | LOW LIGHT FOV (5,5-162mm) FOV 46,5° to 2,2° |  | LWIR FOV (9,8mm) FOV 90° x 70° | 
POWER | 9-36 VDC <2W MAX |  |  |  |  |  | 
OPERATING TEMP | -20°C to +80°C |  |  |  |  |  | 
DIMENSIONS | 90x90x144 (mm) |  |  |  | 100x100x181 (mm) |  | 62x62x85 (mm)
INTERFACE | ETHERNET INTERFACE |  |  |  |  |  | 
CONNECTOR | Hermetic Stainless Steel D38999/23YB35PN |  |  |  |  |  | 
WEIGHT (Kg) | 1.2 kg |  | 1.3 kg |  | 1.4 kg |  | 0.38 Kg
SEALING | Nitrogen Purged |  |  |  |  |  | NONE
IP RATE | IP67 |  |  |  |  |  | IP66
69
xEyeSERIES Rugged LWIR / Low Light Electro-Optic Sensor

## Slide 70
DIMENSIONS: (LxWxH, mm) 90x90x144
WEIGHT: 1.2/1.3 Kg
90
143.82
90
xEye-N Rugged LWIR / Low Light Electro-Optic Sensor

## Slide 71
DIMENSIONS: (LxWxH, mm) 119x160x133.5
WEIGHT: 2.3Kg
xEye-N with Bracket Rugged LWIR / Low Light Electro-Optic Sensor

## Slide 72
DIMENSIONS: (LxWxH, mm) 100x100x181
WEIGHT: 1.4Kg
100
180.6
100
xEye-Z Rugged LWIR / Low Light Electro-Optic Sensor

## Slide 73
DIMENSIONS: (LxWxH, mm) 207x152x145
WEIGHT: 2.4Kg
xEye-Z with Bracket Rugged LWIR / Zoom Day Electro-Optic Sensor with Bracket

## Slide 74
DIMENSIONS: (LxWxH, mm) 62x62x85
WEIGHT: 352g
xEye
Micro Rugged Low Light Electro-Optic Sensor

## Slide 75
BRACKET DIMENSIONS
xEye-BRKT-M/MS
xEye-BRKT-[BT]
M MATTE BLACK RAL 9005 ALUMINUM BRACKET
MS BLACK STEEL BRACKET
Micro Rugged Low Light Electro-Optic Sensor
xEye with Bracket
Micro Rugged Low Light Electro-Optic Sensor

## Slide 76: AIxSERIES Rugged AI NEURAL Processing Unit

## Slide 77
MODEL | AIxNPU | AIxGPU | AIxNPU2 | AIxNPU-360Kit
OS | MICROSOFT WINDOWS 11 | UBUNTU LINUX | MICROSOFT WINDOWS 11 | MICROSOFT WINDOWS 11
CPU | Intel® Core™ Ultra | NVIDIA ORIN 64GB FORECR | Intel® Core™ Ultra | Intel® Core™ Ultra
RAM | 64GB | 64GB | 64GB | 64GB
STORAGE SSD | 1TB | 256GB | 1TB | 1TB
DISPLAY | 2 x HDMI 2.1 TMDS | HDMI 2.0 (MAX RESOLUTION 3840x2160) | 5 x 4K | 2 x HDMI Ports MIL.STD Connector
ETHERNET | 2.5 Gigabit LAN | 1x Gigabit Ethernet | 2.5 Gb Ethernet port | 2.5 Gigabit LAN
PERIPHERIALS | 1 x USB4 2 x M.2 Key M, 1 x M.2 Key E (WiFi-6E Module) 2 x HDMI 2.1 TMDS 1 x DP 2.1 (from Type-C) 1 x DP 1.4a (from Type-C) | 2x USB 3.1 Type-A 1x CAN Bus 1x RS232/422/485 (software configurable) 2x USB-C (Debug/Recovery) 2x Digital Input 3x Digital Output | 2 x USB 3.2 Gen2 Type-A 1 x USB 3.2 Gen2 Type-C 1 x 3.5mm Combo Audio Jack 1 x Thunderbolt 4 Type-C/ DisplayPort TM 2.1 4 x USB 3.2 Gen 2 Type-A 1 x RJ45 LAN 1 x DC-in 1 X Kensington Lock | 1 x USB4 2 x M.2 Key M, 1 x M.2 Key E (WiFi-6E Module) 2 x HDMI 2.1 TMDS 1 x DP 2.1 (from Type-C) 1 x DP 1.4a (from Type-C)BUZZER ALARM
POWER SUPPLY | 9-40VDC-DC POWER SUPPLY WITH EMI FRI FILTER |  |  | 
DIMENSIONS (mm) | 221x225x91 | 228x105x277 | 370x328.3x139 | 248x263x150
OUTPUT VIDEO OPTIONS | HDMI, 2 x FULL HD RTSP (H.264/265) (EMBEDDED HARDWARE) | HD-SDI, HDMI | HDMI 2.1 FRL DP 2.1 | HDMI
77
*Each model is available with a Vento option
AIxSERIES Rugged AI NEURAL Processing Unit

## Slide 78
DIMENSIONS: (LxWxH,mm) 221x225x91
WEIGHT: 6 kg
AIxNPU Rugged AI NEURAL Processing Unit

## Slide 79
DIMENSIONS: (LxWxH, mm) 2 228x105x277
WEIGHT: 8.1kg
79
AIxGPU
Rugged AI Neural Processing Unit

## Slide 80
DIMENSIONS: (LxWxH, mm) 370x328.3x139
WEIGHT: 14 kg
80
AIxNPU2
Rugged AI Neural Processing Unit

## Slide 81
DIMENSIONS: (LxWxH, mm) 248x263x150
WEIGHT: 5 kg
81
AIxNPU-360Kit
Rugged AI Neural Processing Unit